## Slide 1: Improve the robustness of your embedded software by using the Intel Simics virtual platform and hardware fault injection
Virtual Platforms
Nov. 20, 2025
14:10-14:30
Réfectoire
Nicolas VAN SPAANDONCK
Senior Field Application Engineer at Wind River

## Slide 2: Agenda
What is Intel Simics?
Available Simulation Models
Intel Simics Capabilities
Fault Injection:
  By Traffic Interception
  By Memory Operations Interception
  By Devices Error Registers
Cyber-Testing with RESim and Intel Simics
Interesting References
Simics® is a trademark of Intel Corporation or its subsidiaries.

## Slide 3: Deliver better software, faster and at lower cost
Scalable full-system simulation
Runs final target binaries
Enables:
  Hardware and software co-development
  Rapid test and integration
  Ability to inject hardware faults
Increases
  System quality
  System performance
Reduces
  System integration costs
  System lifecycle costs
  System development time
Complete Systems and Networks
Racks of Boards and Backplanes
Complete Boards
Devices and Buses
SOC Devices
Processor and Memory

## Slide 4: Simulate any end-system size in a virtual network
Virtual
Network
Intel® Simics® Simulator
Target Virtual Hardware
Memory
Devices
CPU Core
Storage
Network & I/O
CPU Core
CPU Core
CPU Core
...
Target Software Stack
Host Operating System
Applications and Software Middleware
Drivers and Boards Support Packages (BSP)
Hypervisor / Target Operating System
Host Hardware
Model Library
Intel
Wind River
Customers
Ecosystem
Target Virtual Hardware
Target Software Stack
External I/O
Ethernet
Serial
Keyboard
Mouse
External Tools
Debugging
Testing
Scripting
GUI
C, C++, SystemC, Python, DML
Simics® is a trademark of Intel Corporation or its subsidiaries.

## Slide 5: Intel simics and wind river
Simics is an Intel product, made publicly available since 2022.
Wind River used to be an Intel subsidiary between 2009 and 2018.
Wind River has an agreement to resell Intel Simics with technical support and services.
Simics® is a trademark of Intel Corporation or its subsidiaries.

## Slide 6: Available simulation models
Architecture | Semiconductor | SoCs | Intel Simics 6 | Intel Simics 7 | 
 |  |  | Wind River Edition | Wind River Edition | Intel Public Release
 |  | Recent Core and Xeon models |  |  | 
 |  | Agilex |  |  | 
 |  | Zynq US+ MPSoC |  |  | 
 |  | Versal |  |  | 
 |  | S32G |  |  | 
 |  | LS1 |  |  | 
 |  | Stellar |  |  | 
 |  | TDA4 |  |  | 
 |  | Several cores |  |  | 
 |  | PolarFire SoC |  |  | 
 |  | e300 to e6500 |  |  | 
 |  | LEON3 and 4 |  |  | 
x86
Simics® is a trademark of Intel Corporation or its subsidiaries.

## Slide 7: Intel simics capabilities
Adopt new development techniques not possible with physical hardware, from the smallest to the most complex systems.
Synchronous Stop for Entire System
Reverse Execution, Unlimited Breakpoints
Determinism and Repeatability
Full-System Checkpoint and Restore
Repeatable Fault Injection on Any Component
Scripting and Automation
See Everything, Trace Everything
Real-World Connectivity
Simics® is a trademark of Intel Corporation or its subsidiaries.

## Slide 8: Fault injection in Intel Simics
Fault injection is a technique used to test system robustness by deliberately introducing errors or faults.
Intel Simics allows precise fault injection control over when and where faults are injected at the following levels:
Hardware
Inject faults into memory (e.g. bit flips)
Simulate CPU register corruption
Software
Modify system calls or interrupt behavior
Simulate corrupted data structures or invalid inputs
Environment
Network latency or packet loss
Power failures issues
Emulate device failures (e.g. disk read errors, USB disconnection…)
Simics® is a trademark of Intel Corporation or its subsidiaries.

## Slide 9: fault injection by traffic interception
Intel Simics allows the interception of traffic in the system, including:
Network packets.
Bus transfers.
Memory reads.
Intel Simics
Target HW
Other Target HW
Communications
Device
Fault Injection
Module
(Extension)
Bus or Network Model
Communications
Device
Target OS
Applications
Memory Map
… …
Device
Mapping
Processor
Core
Simics® is a trademark of Intel Corporation or its subsidiaries.
Target OS
Applications
Network Interface
Device Interface

## Slide 10: Example: network packets injection on microchip PFSOC
Let’s load the Ethernet injector component:
> load-module eth-injector-comp
Let’s instantiate it:
> new-eth-injector-comp name = inj0
Let’s connect it to an Ethernet PHY:
> connect pfsoc.phy[0] inj0.link
Let’s inject a Wireshark PCAP log containing a previously recorded ICMP flood:
> inj0.injector.start file = flood.pcap

## Slide 11: fault injection by memory operations interception
Simics® is a trademark of Intel Corporation or its subsidiaries.
Intel Simics
Target HW
Device or Memory
Memory Map
… …
Device
Mapping
Processor
Core
Target OS
Applications
Mapping Interception
Memory
Operation
Fault Injection Module
(Extension)
Change contents of memory operation, before or after it has been processed by its target
Callbacks on all memory operations

## Slide 12: fault injection by Error reporting registers in devices
Simics® is a trademark of Intel Corporation or its subsidiaries.
Intel Simics
Target HW
Memory Map
… …
Device
Mapping
Device Model
Error Registers
Processor
Core
Target OS
Applications
Error Handler Code
Send error interrupt to processor core
Error-handling code reads error register values
Fault Injection Module
(Extension)
Set error registers to appropriate values
Interrupt activates error-handling code

## Slide 13: Example: Injecting ECC Faults in a SPARC V8 CPU
Intel Simics provides an interface called sparc_v8_ecc_fault_injection to simulate uncorrectable ECC faults in SPARC V8 architectures.
These faults trigger exceptions like:
Instruction Access Exception
Data Access Exception
Register Access Error
SIM_INTERFACE(sparc_v8_ecc_fault_injection) {
void (*inject_instr_access_exception)(conf_object_t *cpu);
void (*inject_data_access_exception)(conf_object_t *cpu);
void (*inject_reg_access_error)(conf_object_t *cpu);
};
Simics® is a trademark of Intel Corporation or its subsidiaries.
def inject_fault(cpu_obj):
# Set a breakpoint at a specific instruction or memory location
bp = simics.Breakpoint(address=0xdeadbeef, cpu=cpu_obj)
# Define callback to inject fault
def fault_callback():
simics.inject_data_access_exception(cpu_obj)
print("ECC fault injected at 0xdeadbeef")
# Attach callback
bp.set_callback(fault_callback)

## Slide 14: cyber-testing with resim and intel simics
RESim goals:
  Identify and analyze software that executes on embedded systems.
  Reverse-engineer protocols used by services on those systems.
  Discover and analyze potential vulnerabilities, e.g. via fuzzing.
  Unknown systems (black box) and systems we should know.
RESim features:
  System execution tracing:
    System call tracing with de-referenced parameters.
    Identifies processes, network connections, IPC, etc.
  Dynamic analysis of processes:
    IDA Pro & Ghidra plugins to control execution, e.g. breakpoints.
    Ability to run forwards or backwards to system events.
    Track ingested data through memory transactions and IPC.
    Reverse-track sources of memory or registers.
  AFL Fuzzer integrated with RESim for vulnerability analysis:
    Inject data directly into application or kernel memory.
    Run target to the desired starting state rather than building test harnesses.
Simics® is a trademark of Intel Corporation or its subsidiaries.
https://github.com/mfthomps/RESim

## Slide 15: Interesting References
Public release of the Intel Simics simulator and Get Started Guide
RESim: Reverse engineering using a full system simulator
RESim: Introduction Video
Device Modeling Language
Introducing RISC-V in the Intel Simics Simulator
Simics Simulator Threading with RISC-V Simple
Intel Simics Modeling Extension for Visual Studio Code
Simics Fault Injection Demonstration Video
Simics® is a trademark of Intel Corporation or its subsidiaries.

## Slide 16: Thank you!
Any questions? Please send them to nicolas.vanspaandonck@windriver.com